## Slide 1: LEF Quality Assurance Tool
Abrahim Hamdan
Ash Huang
Benjamin Perry
ECE Department
EE/CPE584 Introduction VLSI

## Slide 2
Background
LEF (Library Exchange Format) file
  Contains abstract layout views of the cells in an IC
  Used by P&R tools to route cells properly.
  Inverter Example --->
TLEF (Technology LEF) Files
  Contains layer definitions, via definitions, and design rules.
  Provides layer types and manufacturing constraints.
Liberty (LIB) Files
  Contain timing and electrical info associated with standard library cells.
  Used by timing and power analysis tools to verify circuit performance.
Layout View
Abstract View
I/O Pins
Obstructions

## Slide 3
Background – LEF Files Hierarchy
VERSION
BUSBITCHAR
DIVIDERCHAR
MACRO 1
- CLASS / SIZE / SYMMETRY
- PIN Statements
- OBS
MACRO 2
MACRO 3
⋮
MACRO N
END LIBRARY
Hierarchy separation “/”
LEF Format Version
Bus Bit indexing “[]”
Cell Definition
I/O Pins with direction,
use, and port geometry
Obstruction layers
with geometries
Defines the cell properties
and dimensions

## Slide 4
Background – TLEF Hierarchy
VERSION
BUSBITCHAR
DIVIDERCHAR
UNITS
SITE
LAYER
  MASTERSLICE
    PWELL, NWELL
  IMPLANT
    VTL_N/P, VTH_N/P
  CUT
    CO, VIA1-VIA8
  ROUTING
    MET1-MET8
VIARULE
Hierarchy separation “/”
LEF Format Version
Bus Bit indexing “[]”
Units of measurements
Defines placement grid for
Std cells.
Base layers for transistors
Defines Threshold
Voltage
Vertical connections
Between metal layers
Horizontal metal
interconnects
Automatic generated
Via array

## Slide 5
Background – LIB Hierarchy
Library Name & Units
Operating Conditions
Cell 1
- Area / Leakage Power
- pin (input)
- Capacitance
- Timing (setup/hold)
- pin (output)
- Function
- Timing (delays, transitions)
- Power (rise/fall power)
Cell 2
Cell 3
⋮
cell N
Defines the library
and measurement units
Defines the process,
voltage, and temp the
the library was characterized
Cell Properties: Physical size
Power consumption when idle
Input Pin Definition
Output Pin Definition
For sequential cells
Boolean Equation
of the output
How fast the
output switched
Dynamic power
consumed

## Slide 6: Provided Script
Quality assurance tool that validates LEF cell library files against Liberty and technology files for DRC compliance.
The provided script can:
Parses and sorts LEF files: Reads LEF files and sorts cells, pins, and properties in a consistent order.
Cross-checks LEF against LIB files: Compares cells and pins between LEF and Liberty files to find mismatch cells and pins.
Validates LEF file syntax and completeness: Checks to see if the direction for pin properties matches

## Slide 7: Script Command Lines
To run the script:
  ./lef_QA.rb -w <workspace_dir> # Specify working directory
  ./lef_QA.rb -t <tech.tlef> # Specify technology LEF
  ./lef_QA.rb -l <liberty_dir> # Specify liberty file directory
  ./lef_QA.rb -s <file.lef> # Only sort LEF file
  ./lef_QA.rb -i <file.lef> # Skips printing large errors (>1000)
  ./lef_QA.rb –h # Outputs the help manu
Cannot run –w with –s.
Can run –s with –l and –t. For example:
./lef_QA.rb -s <file.lef> -l <liberty_dir> -t <tech.tlef>

## Slide 8: Script Output
After executing the script, it outputs three files:
Sorted LEF file (*_sorted)
  Rewrites the LEF file with cells sorted alphabetically.
  Orders cell properties consistently (CLASS, ORIGIN, SIZE, etc.).
  Sorts pins alphabetically within each cell.
Error Report file (*_errors)
  Lists missing required properties.
  Reports mismatches between LEF and Liberty files.
  Flags syntax issues.
Comments file (*_comments)
  Extracts all comments lines from LEF file.

## Slide 9: Script Output
The script also outputs all different types of tests to validate LEF properties, LEF syntax, and mismatches between LEF and LIB.
Test Number
Test Name
Indicates if test passed or failed

## Slide 10
Not sorted
Sorted
Original LEF:
After Sorting:
12/19/2025
EE/CPE584 Intro to VLSI
10
Script Output – Sorted LEF File

## Slide 11
12/19/2025
EE/CPE584 Intro to VLSI
11
Script Output – Error LEF File
Test Number
Test Name
Warning or error output
Line number for error
Cell name for error
Pin name for error
Notes: Bobby

## Slide 12: Script Flowchart Part 1
Parse Command Line Argument
Scan for LEF and TLEF files
Parses TLEF
to get layers
Parses LEF file
For each Macro
  Extract properties
  For each pin
    Extract direction, use and port.
    Extract OBS
Sort LEF using cells, pins, properties
Next slide
Start

## Slide 13: Script Flowchart Part 2
Previous Slide
Parse LIB file
Extract cells, pins, area, and direction.
Yes
Compare LEF with LIB
Cells exists in both?
Pins exists in both?
Area matches the Size?
Pin direction matches?
Validate LEF File for:
For any missing properties
Unknown Layers
Syntax Errors
No
Generate Output Files:
Sorted LEF file
Error Report
Comments file
LIB file provided?
End

## Slide 14: Problem Statement
LEF-LIB Data Consistency
  No comprehensive comparison between physical layout (LEF) and logical timing (LIB) files.
VIA Layer Validation Gap
  No validation to ensure VIAs in cell pins have corresponding OBS layers.
Code Maintainability Issues
  Poor code readability makes maintenance, debugging, and enhancement difficult.

## Slide 15: LEF-LIB Compare

## Slide 16: Previous Script Outline
Previous LEF-LIB Comparison Script:
  compared cell dimensions (LEF SIZE vs LIB area properties)
  verifies pin exist in both files.
Issues:
  Limited Scope: Only checks geometric properties and pin existence, missing pin verification.
  Lack of communication to users: Does not inform user of what is causing the errors
  Pin existence incorrect
    reports ground and power pins missing despite being in both LEF and LIB files

## Slide 17: Previous Script’s Error file showing Pins Missing Errors
Previous implementation Issue:
Say that Lef is missing all ground and power pins despite being defined in both Lef and lib
Cell a21110_1 pins in Lef
Cell Name
Pins “missing”
Output of Errors File
Notes: Define what the error is , what caused it before and how i fixed it up. Highlight the errors

## Slide 18: Cause of Issue for the Pin Missing Errors
Start
Lef Files Processing
Lib Files Processing
Lef_pins= Lef_Pins. Upcase();
Output Lib_pins = Lib_pins.Upcase;
Output Lib_pins = pg_pins;
Does Lef_pins == Lib_pins?*
*Error:
Lower case pg_pins in lib are compared to upper case pins in lef, causing errors to be thrown out and the program to identify pins to be missing from one file

## Slide 19: Solution to Issue for Pins Missing Errors
Start
Lef Files Processing
Lib Files Processing
Output Lef_pins= Lef_Pins. Upcase();
Output Lib_pins = Lib_pins.Upcase;
Does Lef_pins == Lib_pins?*
*Solution:
Make all parsed pins uppercase to prevent case sensitivity issues

## Slide 20: Updated Script’s Error File after uppercase correction
Only shows pins that are truly in one file and not the other
Provides the cell name, pin name and the lib file they are not in
Cell of missing pin
Missing Pin name
Liberty file of missing pin

## Slide 21: Previous Script Showed a lack of detail on why the liberty incorrect pin property failed
Output of Errors File
Script tells that there are cell properties missing in both scripts but does not display:
  Which cell
  What properties
  What caused the mismatch/fail

## Slide 22: Initial Implementations for Property Comparison
Start
Issues:
*Only Directions is compared despite having a loop going through all properties
**Value of each property must match exactly (ex. Input = Input) leaving limited comparison between two files
***Returns fail but does not imply or explain what caused fail
Input Lib_pin;
Input Lef_pin;
Input Lib_pin_property;
Input Lef_pin_property;
*Lib_pin == Lef_pin?
**Lib_pin_property == Lef_pin_property?
***Output failed;
No
No
Yes;
Next pin

## Slide 23: New Implementations
The new script current supports comparisons for
  Cells:
    Area - Ensures Area from LIB files matches the Areas from LEF files
  Pins:
    Direction – ensures directions from both LIB and LEF matches
    Clock – Verifies LIB clock pin aligns with LEF “USE” property
    PG_Type – Verifies LIB power or ground pins aligns with “USE” properties
    Voltage_Name – ensures the voltage name in LIB is consistent
    Related_Power_Pin / Related_Ground_Pins – validates References between power and ground properties between pins in the LIB file.

## Slide 24: New Implementation Flowchart
Start
Case Comparison_Type
Voltage_Name
Next Slide
Voltage_name == pin name?
End
Output Error;
False
True

## Slide 25: New Implementation Flowchart
Related_Power
Related_Ground
Previous Slide
Next Slide
Related_Power == VPWR || VPB
Related_Ground == VPWR || VPB
End
Output Error;
False
False
True
True

## Slide 26: New Implementation Flowchart
Direction
Previous Slide
Next Slide
Lef_Direction == Lib_Direction
End
Output Error;
False
True

## Slide 27: New Implementation Flowchart
Clock
Previous Slide
Next Slide
LEF_USE == CLOCK;
LIB_CLOCK == TRUE;
LEF_USE != CLOCK;
LIB_CLOCK == FALSE;
LEF_USE != CLOCK;
LIB_CLOCK == TRUE;
LEF_USE == CLOCK;
LIB_CLOCK != TRUE;
Output Error;
End

## Slide 28: New Implementation Flowchart
PG_Type
Previous Slide
End
Input LEF_USE = Power
Input Lef_USE = Ground
PG_Type = PRIMAR_GROUD
PG_Type == PRIMARY_POWER
End
Output Error;
False
False
True
True

## Slide 29: New Implementation Error File
Type of mismatch
LEF File
Name
Pin name
Cell Name
Details of Mismatch
Current Name
*note: Lib File purposely edited to create errors to test

## Slide 30: VIA Obstructions
The current script does not ensure that all cell VIAS have OBS layers associated with them.
Script needs to be updated to perform the following:
  Identifies VIA definitions within cells in the Pin/Port section.
  Verifies that VIAS have associated OBS layers.
The purpose for VIA OBS checking is to help prevent routing conflicts during physical design.

## Slide 31: VIA Obstructions
Updated the script to perform the following:
Detect Via statements during LEF parsing.
  Checks the PIN/PORT section of the cell
Store Via information.
Validate Vias have associated OBS layer.
  Does this by checking every layer in the OBS section of the cell
Report error when Via layer is not included.

## Slide 32: VIA Obstructions TLEF file
LAYER
  MASTERSLICE
    PWELL, NWELL
  IMPLANT
    VTL_N/P, VTH_N/P
  CUT
    CO, VIA1-VIA8
  ROUTING
    MET1-MET8
The script parses all the CUT layers and stores its information.

## Slide 33: VIA Obstructions LEF file
MACRO
- CLASS / SIZE / SYMMETRY
- PIN Statements
    PORT
      Layer VIA
        VIA Geometry
- OBS
    Layer VIA
      VIA OBS Geometry
1. The script parses all the Pins/Ports to see if there are via layers. If there is, the script saves that via Information.
2. The script then goes to OBS section and checks all the layers. If there is no VIAs, the script will report an error. If VIAs exist, it passes the test.

## Slide 34: VIA Obstructions Flowchart Part 1
Is TLEF file provided
Parse TLEF
Extract all Cut layers
Parse LEF File
Yes
No
Next Slide
Start
“Warning: NO TLEF Found”
Use predefined layers

## Slide 35: VIA Obstructions Flowchart Part 2
For each Layer in Pin/Port
Yes
No
Previous Slide
Skip
Store Pin and Layer Name
No
Yes
No
Yes
Is Layer a Cut Layer?
Cut Layers Found?
Cut Layers in OBS?
End
“Passes Via OBS checking test”
“Passes Via OBS checking test”
“Error: Cut Layer missing from OBS”

## Slide 36: VIA Obstructions Output Part 1
Tested the script with provided LEF and TLEF files.
Output:
Failed the Via OBS checking.
Added the error to the error log file.
Outputs all layers collected
Number of Cut
And Routing layers

## Slide 37: VIA Obstructions Output Part 2
The output from LEF error log file:
Error line number
Reason why it failed the test
Cell name Pin name Layer name Number of Vias in that layer

## Slide 38: VIA Obstructions Output Part 3
Pin X from the LEF file:
2. We can see that VIA 4 does not have an
associated layer in OBS section.
1. Checking if VIA4 has an
associated OBS layer

## Slide 39: Code Readability
Encapsulation:
  Problem: The original script used global file handling and manual line tracking, making it fragile and hard to debug.
  Solution: Implemented the FileCursor class. This object-oriented approach encapsulates the file reading logic, keeping the current line and index safe and consistent.
Modularization:
  Problem: The logic for parsing files and comparing them was mixed into one massive procedural block.
  Solution: Extracted distinct responsibilities into named methods like parse_lef_files, parse_lib_files, and compare_lef_lib.
Safe Resource Management:
  Problem: Files were opened manually and risked remaining open if the script crashed.
  Solution: Converted file operations to use Ruby's block syntax (File.open(...) do |file|), ensuring all files close automatically even if errors occur.

## Slide 40
# | TODO Description | Status | Notes
1 | Wrap file/index in PBR_Int | ✅ DONE | Replaced with object-oriented FileCursor class
2 | Collect get_current_line methods | ✅ DONE | Replaced with object-oriented FileCursor class
3 | WS DIR Parsing needs method | ✅ DONE | Logic extracted into modular functions to parse_ws_dir.
4 | LEF Parsing needs method | ✅ DONE | Logic extracted into modular functions to parse_lef_files.
5 | Lib Parsing needs method | ✅ DONE | Logic extracted into modular functions to parse_lib_files.
6 | LEF-LIB Compare needs method | ✅ DONE | Logic extracted into modular functions to compare_lef_lib.
7 | Print file needs method | ✅ DONE | Logic extracted into modular functions to print_output_files.
8 | Use block format for File.open | ✅ DONE | Implemented in print_output_files. Implemented block syntax to auto-close files.
9 | Cell properties: case vs if/else | ✅ DONE | Refactored Cell to use case.
10 | Cell print: Writing to file inadvisable | ✅ DONE | Refactored to to_s.
11 | Layer checks: Make TLEF required | ✅ DONE | TLEF parser now correctly extracts CUT/ROUTING layers.

## Slide 41
# | TODO Description | Status | Notes
12 | Lib parsing: area/pins/direction | ✅ DONE | Parses completed and all cells, pins and properties parsed properly
13 | PG_PIN check (PWR/GND) | ✅ DONE | Implemented in LibRuleChecker class
14 | Pin Init: Should not do work | ✅ DONE | Logic moved to new parse() method.
15 | Uncommon properties: Deprecate | ✅ DONE | Function deleted and calls removed.
16 | Collect rules in LibRuleChecker | ✅ DONE | Moved to LibRuleChecker class
17 | Errors: Print file-to-file | ❌ NOT DONE | Still prints large block output (Low priority).
18 | Cell Sort: Should be private | ✅ DONE | sort! is now private and automatic.
19 | Cell Source: SOURCE syntax check | ✅ DONE | Logic removed/deprecated during cleanup.
20 | Add missing_source error key | ✅ DONE | Logic removed/deprecated during cleanup.
21 | Layer Sort: coordSort private | ✅ DONE | sort! is now private and automatic.
22 | Pin Init: Separate function | ✅ DONE | Logic moved to new parse() method.

## Slide 42: Refactoring Impact
Before:
  Procedural "spaghetti code."
  Global variables for file tracking.
  Manual array indexing (e.g., line[index+1]).
After:
  Object-Oriented Design: FileCursor and LibRuleChecker classes manage their own data.
  Scalability: New checks (like the VIA OBS check) were easy to add because the parsing logic is now separate from the checking logic.
  Maintainability: Future teams can work on compare_lef_lib without breaking the file reader.

## Slide 43: Summary
Improved LEF vs LIB by implementing pin property checks for direction, clock, pg_types and related ground and power references
Added Via Obstruction checking to help prevent routing conflicts during physical design.
  Completed by parsing CUT layers from TLEF and PORT sections from LEF, then verifies Via layers exist in OBS sections.
Refactored codebase for maintainability
  Transformed a procedural script into an Object-Oriented application by implementing a FileCursor class, modularizing file processing, and resolving over 20 legacy TODO items to reduce technical debt.

## Slide 44: Possible Future Work
Set up CONFIG file
  The goal is to move options from command-line flags to a more permanent configuration file.
Investigate SOURCE USER
  Figure out what to do with the SOURCE property which are still in the Cell class.
Research SI2 LEF/DEF APIs
  This is a research task to see if an external API would be better than this custom script.
Update Flowchart
  Need to update flowchart for the changes made in TLEF/TF parsing , LEF vs LIB, LEF parsing for VIAs, and checking of VIAs in OBS.
Modular File Architecture
  Current State: The ruby file is currently a single "monolithic" script holding all logic (parsing, data models, comparison, and reporting).
  Proposed Change: Split the script into a standard library structure:
    lib/parsers/: Separate files for FileCursor, TLEF_File, and Liberty_Cell.
    lib/models/: Separate files for Cell, Pin, and Layer.
    lib/reporters/: Logic for printing errors and sorted files.
  Benefit: Allows multiple developers to work on various parts of the tool simultaneously without merge conflicts.

## Slide 45
Backup Slides For The Rest
Acquired From Previous Team (S22)

## Slide 46: Possible Future Work - SOURCE USER Syntax
scs8ls_lpflow_s8p.lef
  LEF/DEF syntax v5.5
  Each macro specifies a SOURCE property
LEF/DEF language reference v5.7, v5.8
  SOURCE property not part of LEF syntax
  Only part of DEF syntax
DEF Syntax:
  SOURCE specifies source of component
  USER specifies component is generated by user
LEF QA Script
  Includes SOURCE as one of the possible LEF syntax keywords
  Doesn’t throw errors when SOURCE is included in LEF files
Need to do further research and determine scope of this problem

## Slide 47: Possible Future Work - SI2 LEF/DEF APIs
Silicon Integration Initiative (SI2)
  Formerly CAD Framework Initiative (CFI)
  Non-profit consortium of semiconductor, systems, EDA, and manufacturing companies
  https://si2.org/
  Distributes LEF/DEF APIs in C/C++
LEF/DEF APIs
  Created and updated by Cadence
  Used to read, write, and manipulate LEF/DEF files
  APIs can parse all LEF syntax keywords
Need to explore APIs more and determine tradeoffs for adopting

## Slide 48
Updated Keyword Discrepancies
[VERSION statement]
[BUSBITCHARS statement]
[DIVIDERCHAR statement]
[VIA statement] …
[SITE statement]
[MACRO statement] …
[BEGINEXT statement] …
[END LIBRARY]
{LAYER layerName
[EXCEPTPGNET] [SPACING minSpacing | DESIGNRULEWIDTH value] ;
[WIDTH width ;]
{PATH [MASK maskNum] pt ... ;
| PATH [MASK maskNum] ITERATE pt ... stepPattern ;
| RECT [MASK maskNum] pt pt ;
| RECT [MASK maskNum] ITERATE pt pt stepPattern ;
| POLYGON [MASK maskNum] pt pt pt pt ... ;
| POLYGON [MASK maskNum] ITERATE pt pt pt pt ... stepPattern ;
} ...
| VIA [MASK viaMaskNum] pt viaName ;
| VIA ITERATE [MASK viaMaskNum] pt viaName stepPattern ;
} ...
12/19/2025
EE/CPE584 Intro to VLSI
48
Keyword Highlighting:
Only in LEF files
No highlighting - In both script and LEF files

## Slide 49
Updated Keyword Discrepancies
MACRO macroName
[CLASS
{ COVER [BUMP]
| RING
| BLOCK [BLACKBOX | SOFT]
| PAD [INPUT | OUTPUT |INOUT | POWER | SPACER | AREAIO]
| CORE [FEEDTHRU | TIEHIGH | TIELOW | SPACER | ANTENNACELL | WELLTAP]
| ENDCAP {PRE | POST | TOPLEFT | TOPRIGHT | BOTTOMLEFT | BOTTOMRIGHT}
}
;]
[FIXEDMASK ;]
[FOREIGN foreignCellName [pt [orient]] ;] ...
[ORIGIN pt ;]
[EEQ EEQmacroName ;]
[SIZE width BY height ;]
[SYMMETRY {X | Y | R90} ... ;]
[SITE siteName [sitePattern] ;] ...
[PIN statement] ...
[OBS statement] ...
[DENSITY statement] ...
[PROPERTY propName propVal ;] ...
END macroName
12/19/2025
EE/CPE584 Intro to VLSI
49
Keyword Highlighting:
Only in LEF files
No highlighting - In both script and LEF files

## Slide 50
Updated Keyword Discrepancies
[PIN pinName
[TAPERRULE ruleName ;]
[DIRECTION {INPUT | OUTPUT [TRISTATE] | INOUT | FEEDTHRU} ;]
[USE { SIGNAL | ANALOG | POWER | GROUND | CLOCK } ;]
[NETEXPR "netExprPropName defaultNetName" ;]
[SUPPLYSENSITIVITY powerPinName ;]
[GROUNDSENSITIVITY groundPinName ;]
[SHAPE {ABUTMENT | RING | FEEDTHRU} ;]
[MUSTJOIN pinName ;]
{PORT
[CLASS {NONE | CORE | BUMP} ;]
{layerGeometries} ...
END} ...
[PROPERTY propName propVal ;] ...
[PROPERTY LEF58_VIAINPINONLY “VIAINPINONLY ; ” ;]
[ANTENNAPARTIALMETALAREA value [LAYER layerName] ;] ...
[ANTENNAPARTIALMETALSIDEAREA value [LAYER layerName] ;] ...
[ANTENNAPARTIALCUTAREA value [LAYER layerName] ;] ...
[ANTENNADIFFAREA value [LAYER layerName] ;] ...
[ANTENNAMODEL {OXIDE1 | OXIDE2 | OXIDE3 | OXIDE4} ;] ...
[ANTENNAGATEAREA value [LAYER layerName] ;] ...
[ANTENNAMAXAREACAR value LAYER layerName ;] ...
[ANTENNAMAXSIDEAREACAR value LAYER layerName ;] ...
[ANTENNAMAXCUTCAR value LAYER layerName ;] ...
END pinName]
12/19/2025
EE/CPE584 Intro to VLSI
50
Keyword Highlighting:
Only in LEF files
No highlighting - In both script and LEF files

## Slide 51
Updated Keyword Discrepancies
[OBS
{LAYER layerName
[EXCEPTPGNET]
[SPACING minSpacing | DESIGNRULEWIDTH value] ;
[WIDTH width ;]
{ PATH pt ... ;
| PATH ITERATE pt ... stepPattern ;
| RECT pt pt ;
| RECT ITERATE pt pt stepPattern ;
| POLYGON pt pt pt pt ... ;
| POLYGON ITERATE pt pt pt pt ... stepPattern ;
} ...
| VIA pt viaName ;
| VIA ITERATE pt viaName stepPattern ;
} ...
END]
12/19/2025
EE/CPE584 Intro to VLSI
51
Keyword Highlighting:
Only in LEF files
No highlighting - In both script and LEF files

## Slide 52: VIA Obstructions Fallback Patterns Part 1
Fallback patterns used for Cut and Routing layers:
Cut Pattern | Example
/^VI\d*$/i | VI, VI1, VI2
/^VIA\d*$/i | VIA, VIA1, VIA2
/^V\d+$/i | V1, V2, V12
/^CUT\d*$/i | CUT, CUT1, CUT2
/^CONT$/i | CONT
/^MCON$/i | MCON
/^CONTACT$/i | CONTACT
/^CO$/i | CO
Routing Pattern | Example
/^ME\d+$/i | ME1, ME2, ME12
/^MET\d+$/i | MET1, MET2
/^METAL\d*$/i | METAL, METAL1, METAL2
/^M\d+$/i | M1, M2, M9
/^LI\d*$/i | LI, LI1
/^AP\d*$/i | AP, AP1

## Slide 53: VIA Obstructions Fallback Patterns Part 2
The warning comment if no TLEF file is passed: